ABSTRACT
This is the report of our semester final project of the Circuit lab .This
report will give the reader an overview about the steps which are involved
in the making of a Colpitt oscillator. The project is about the making of
Colpitt oscillator that will generate approximately 1 MHz frequency. In
which the following components capacitor, inductor, resistors and
transistor were used. First, the circuit is implemented on PSPICE to test
the circuit whether it giving the correct value or not. Then it was
implemented on breadboard. The frequency and waveform on
oscilloscope were accurate. For making PCB design the software PCB
wizard has been used. For testing the circuit oscilloscope was used. It
showed the output of circuit and showed the waveform of approximately
1 MHz.